## Slide 1: EBGN645: Day 5

## Slide 2: Questions/Comments
Questions:
Can I do my project on X?
Getting data out of GAMS
Using Python/Julia/…
  Will commit examples of each in the repo
  Guest lecture for GAMSPy
Readings
Comments:
  Presenting on recent work: Friday 9/27, 10-11:30AM
    Model development, 111, CCS, electricity policy, …
  Purpose of homework

## Slide 3: Agenda for today
Note on Franzi’s forestry
Conditionals, sparse matrix constructions
Electricity example(s)
  Very simple
  Less simple but still simple
  Adding demand elasticity
  Taking on non-linearities
Longer term
  Ramsey model
  Natural gas model
  Duality, conversions to MCPs

## Slide 4: Why conditionals?
Example, in ReEDS we have indices:
: technology (~200)
: vintage (~100-400)
: region (50 or 134 or 1000s)
: timeslice (330)
: year/time (20-40)
Variable for generation is
Max dimensions = 200*400*134*330*40 = 141,504,000,000
... of which <1% are relevant
For big models, do not trust CPLEX/GUROBI to do the job for you…

## Slide 5: More specifically: sparse matrix construction
Put simply: We do not want to burden the model with irrelevant constraints or decision variables
In GAMS, reducing equation population via…
eq_caplim(i,v,r,h,t)$valid_generation(i,v,r,h,t)..
and reducing variable consideration via:
… + sum{(i,v,r,h,t)$valid_generation(i,v,r,h,t), GEN(i,v,r,h,t) }

## Slide 6: GAMS does not export zeros
Two options if you really need them:
Use a 1e-8 then round to the >=7th decimal in your post-processing.
When need more often, I usually do something like this:
From terminal:
gams myprogram.gms (export the gdx file ‘mydata.gdx’)
gdxdump mydata.gdx format=csv symb=report_parameter > report_parameter.csv
… then have a python program:
def popzero(df,value):
df.pivot(*df.columns).fillna(0).stack().to_frame(value).reset_index()
data_in = pd.read_csv(‘report_parameter.csv’)
data_withcombos = popzero(data_in,’val’)
Special thanks to:
https://stackoverflow.com/questions/58962237/pandas-create-missing-combination-rows-with-zero-values

## Slide 7: Example 4: Elmo’s Electricity
Elmo runs a small electricity utility with two regions. He has three electricity facilities: coal, gas, and wind. Each technology has its own cost and capacity. He must meet the hourly demand of his small towns that are connected via a single transmission line. What is Elmo’s cost-minimizing set of operational decisions?

## Slide 8: Elmo’s Electricity [I] – Sets and parameters
Sets/indices:
: Technology type,
: Variable renewable energy technologies
: Hour of day,
: Region,
: valid combination of technology/region/hour
Parameters
: Cost of generation ($s / MWh)
: Capacity of generation (MW)
: Demand from consumers (MWhs)
: Capacity factor for electricity generation (unitless)
: transmission line capacity (set at 5 MW)
: transmission line loss rate (assumed at 5%)

## Slide 9: Elmo’s electricity [II] - data
See spreadsheet - EBGN645_Data_Elmo.xlsx
Getting data into GAMS… starting simple with CSVs.. all sorts of ways

## Slide 10: Elmo’s Electricity [III] – Variables and objective
Variables:
: Generation in hour (MWh)
: Transmission from to (MWh)
: Total cost, target of our optimization ($s)
Objective:

## Slide 11: Elmo’s Electricity [IV] - Constraints
Total amount of electricity generated must equal/exceed demand:
Cannot generate more than there is capacity for:
Transmission capacity limit:

## Slide 12: Another use of aliases
Say electricity generation in one hour cannot deviate a certain amount from electricity generation in another hour. This has been used previously for unit commitment representation.
New parameter: denotes the deviation allowance from one period to the next across the entire day
Mathematically:

## Slide 13: A (slightly) more complicated model
A simple model of the Colorado/Wyoming electricity dispatch
  24-hour time period
  Unit-level resolution
  Adding on emissions policies
Grabbing data from 2018 – Unit-level capacity, costs, and heat rates
  Happy to talk ReEDS data
Average hourly demand – Use of a global
Important to understand: We will eventually convert this to an MCP
Currently: no transmission

## Slide 14: Electricity dispatch problem
Indices:
: State
: Generation technology
: Unique plant ID
: Hour of day
: valid combination of
: states facing an emissions limit
: states facing an emissions rate limit

## Slide 15: Parameters
: ONM costs ($/mwh)
: unit heat rate (mmbtu / mwh)
: capacity factor (% of nameplate capacity)
: fuel cost ($/mmbtu)
: Capacity (MW)
: Demand per hour (MWh)
: emissions rate (tonnes per MWh)
: state-level emissions cap (tonnes )
: combined state emissions cap (tonnes )
: state-level emissions standard (tonnes per MWh)
: combined state emissions standard (tonnes per MWh)

## Slide 16: Variables, Objective
Variables:
: Generation (MWh)
: cost ($s)
Objective:

## Slide 17: Constraints - basics
Generation capacity limit:
Demand must be met:

## Slide 18: Constraints – Mass-based Policies
State-level emissions limit:
Combined state emissions limit:

## Slide 19: Constraints – Rate-based Policies
State-level emissions rate limit:
Combined state emissions rate limit:

## Slide 20: Limitations of LPs
Why are the mass- and rate-based emissions policy results the same?
How do we overcome this?
LPs -> NLP
Linearizing non-linear functions
NLP examples:
Natural gas extraction
Ramsey growth model
Anything else?